## Slide 1: Radiation and The Geiger-Müller Counter
Joe Belarge

## Slide 2: What is Radioactivity
Radioactive Decay is a spontaneous process in which nucleons are emitted from, or transformed within the nucleus, resulting in a change in the identity of the nucleus, and usually accompanied by the emission of one or more types of radiation from the nucleus and/or atom.

## Slide 3: Why Are Some Nuclei Radioactive?
Nature is lazy  It wants to be in the lowest energy state.
Neon lights are analogous to nuclear radiation (and emit electro-magnetic (EM) radiation).
Ne

## Slide 4: Types of Radiation
Alpha

## Slide 5: Types of Radiation
Alpha
Neutron

## Slide 6: Types of Radiation
Alpha
Neutron
Beta

## Slide 7: Types of Radiation
Neutron
Alpha
Beta
Gamma

## Slide 8: Types of Radiation
Alpha
Neutron
Beta
Gamma

## Slide 9: Types of Radiation
Alpha
Neutron
Beta
Gamma
The 241Am will α-decay, and these α particles will be captured by the 9Be in the AmBe source.

## Slide 10: Types of Radiation
Alpha
Neutron
Beta
Gamma
The 241Am will α-decay, and these α particles will be captured by the 9Be in the AmBe source.
13C* will de-excite through neutron emission.

## Slide 11: Types of Radiation
Alpha
Neutron
Beta
Gamma
The 241Am will α-decay, and these α particles will be captured by the 9Be in the AmBe source.
13C* will de-excite through neutron emission.
Neutron capture will happen on 107,109Ag, creating radioactive 108,110Ag.

## Slide 12: Types of Radiation
Alpha
Neutron
Beta
Gamma
The 241Am will α-decay, and these α particles will be captured by the 9Be in the AmBe source.
13C* will de-excite through neutron emission
Neutron capture will happen on 107,109Ag, creating radioactive 108,110Ag.
108,110Ag will β- decay to 108,110Cd*.

## Slide 13: Types of Radiation
Alpha
Neutron
Beta
Gamma
The 241Am will α-decay, and these α particles will be captured by the 9Be in the AmBe source.
13C* will de-excite through neutron emission.
Neutron capture will happen on 107,109Ag, creating radioactive 108,110Ag.
108,110Ag will β- decay to 108,110Cd*.
108,110Cd* will de-excite through γ-ray emission, and the γ-rays will be detected in the Geiger Müller counter.

## Slide 14: Radioactive Decay
If a radioactive sample contains radioactive nuclei, the amount of nuclei at time t is given below, with λ defined as the decay constant.
The Half-life of a radioisotope is determined by solving the above equation.

## Slide 15: Detecting Radiation
Often it is very difficult to directly detect radiation. It is much easier to detect the ionization of atoms in a detector material that is caused by the radiation we are interested in.
There are many ways to do this, but the goal is always to collect charge carriers.
+
-

## Slide 16: Detecting Radiation
Often it is very difficult to directly detect radiation. It is much easier to detect the ionization of atoms in a detector material that is caused by the radiation we are interested in.
There are many ways to do this, but the goal is always to collect charge carriers.
+
-
+
+
+
-
-
-

## Slide 17: Detecting Radiation
Often it is very difficult to directly detect radiation. It is much easier to detect the ionization of atoms in a detector material that is caused by the radiation we are interested in.
There are many ways to do this, but the goal is always to collect charge carriers.
+
-
+
+
+
-
-
-

## Slide 18: Detecting Radiation
Often it is very difficult to directly detect radiation. It is much easier to detect the ionization of atoms in a detector material that is caused by the radiation we are interested in.
There are many ways to do this, but the goal is always to collect charge carriers.
+
-
+
+
+
-
-
-

## Slide 19: Detecting Radiation – Gas Detectors
Ion Chambers – Radiation passing through gas creates electron-ion pairs that are collected to create the signal.

## Slide 20: Detecting Radiation – Gas Detectors
Proportional Counters – Radiation creates electron-ion pairs, and the accelerated electrons create an avalanche of ionizations that are proportional to the original charge.

## Slide 21: Detecting Radiation – Gas Detectors
Geiger Müller Counter – A higher electric field is applied than for proportional counter or ion chambers, resulting in many more avalanches.
The end signal is independent of the original number of electron-ion pairs produced in the gas.
No energy information! Only works for counting!

## Slide 22: Todays Experiment – Measuring the Half-life of 108,110Ag
Measure counts in the GM tube as a function of time.
From the histogram calculate the lifetime of the Ag isotopes.

## Slide 23: Todays Experiment – In the Real World
Physicists at NSCL use the same technique to measure the lifetime of unknown nuclear states using the Hodoscope.
K. Wimmer et al., NIMA 769, 65-71 (2015)

## Slide 24: Questions
Thanks to everyone at PAN, NSCL, and BPS for making this possible, including:
P. C. Bender, S. Ayoub, C. Fry, K. Childers, Z. Constan, M. Olsen, S. Tessmer