## Slide 1: Update of Prototype AT-TPC
May 20, 2010
Weekly meeting
Claire Hewko, NSCL

## Slide 2: Negative cross talk
Run 202 He+CO2(30%) 1 atm, 241Am
Event 3
Time bin
ASIC Channel
α
Cross talk signal with negative polarity
Almost identical amplitude

## Slide 3: What solutions to reduce the negative cross talk
3 proposals:
  Reduce the impedance of the PA
  Increase the total capacitance between the mesh and the pads
  Do both

## Slide 4: The Pre-Amplifier before any changes
pad
Radd
20 nF
mesh
Ctot = 1nF

## Slide 5: The Pre-Amplifier before any changes
The positive signal is around 1 000 counts
The Negative cross talk represents 200 counts

## Slide 6: Reduce the total impedance of the PA
16 nF
pad
mesh
Radd
Cdet
Radd = 5 MΩ to 0 Ω
Cdet = 20 nF to 0.1nF
Results :
The positive signal didn’t move : also 1000 counts
The negative cross talk = 50 counts for each impedance value
The noise from the output PA is acceptable: the trigger is effective

## Slide 7: Increase the total capacitance between the mesh and the pads
20 nF
pad
mesh
10nF
Ctot = 1nF + 10nF
Quantitatively :
Cpad/Ctot is proportional to the negative cross talk
Expectation with the 10nF capacitance : reduction of the negative signal from 200 counts to 20 counts
Results :
The negative cross talk = 20 counts for the 10nF capacitor

## Slide 8: Both: we have to try
20 nF
pad
mesh
Radd
Cdet
10nF