## Slide 1: NSCL Nuclear Research at MSU
A world-class facility for nuclear experimentation and theory
ISO 9001, ISO 14001, OHSAS 18001 registered
NATIONAL
SUPERCONDUCTING CYCLOTRON LABORATORY
Dr. Zach Constan
NSCL Outreach Coordinator

## Slide 2: Useful information
Location of bathrooms!
If you have minors in your group, your leader must complete a permission form.
Photography is not allowed on the tour, but we have a designated location for a group photo if you want.
You are not expected to know or understand everything! It’s OK.
Stopping us to ask questions is encouraged!

## Slide 3: We study the atomic nucleus
Example: A Helium Atom
Electron
Neutron
Proton
NSCL scientists study the atomic nucleus
Notes: (Have audience identify parts of the atom) At NSCL, we study the nucleus of the atom. Specifically, we study nuclei that are rare, unstable.

## Slide 4: The nucleus is SMALL
An atomic nucleus is as small compared to you…
…as you are compared to our ENTIRE solar system
We can’t see the nucleus, so it’s hard to work with.
But we’ve still found clever ways to control and study it!
Notes: The nucleus is really small, can’t see even with the most powerful microscopes. It’s as small compared to you as you are compared to the ENTIRE SOLAR SYSTEM.

## Slide 5: LEADING SCIENTIFIC ADVANCEMENT
Coupled cyclotron facility and experimental beam lines
Five stories tall
~140 meters (450 feet) long
A person

## Slide 6: Serving the FRIB User Community
NSCL is a world class research facility, supported by the National Science Foundation (NSF), that hosts ~1400 scientists from 50+ countries.
Experiments 24 hours/day, >4000 hours/year
Average experiment lasts ~1 week
About half (30-40) of proposed experiments are approved

## Slide 7: Actual Experiments at NSCL
Calibration of satellite sensors
Fusion with neutron-rich nuclei
DNA changes under radiation (for astronauts and cancer patients)
Nuclear reactions in dying stars
Isotope harvesting for medical use
Harvetting

## Slide 8: Why pay for nuclear research? (or, “Who cares?”)
It keeps us healthy
It tells us more about our world
It makes electricity
What we learn about the nucleus can
save lives and change the world!
Plus: smoke detectors, smartphones, safer food, etc.

## Slide 9: Who works at NSCL?
800+ employees
Theorists
and Experimenters
Undergraduate and
Graduate students
Facility operators
Technicians and machinists
Research & Development (inventing)
Designers and engineers
  Our employees come from backgrounds in nuclear science, physics, chemistry, all types of engineering, computing, mathematics, welding, machining, construction, etc…
  We represent most fields of Science, Technology, Engineering and Math (STEM)!

## Slide 10: Education and Outreach
NSCL has the
#1 ranked nuclear science program
among US graduate schools
(U.S. News & World Report, 2014)
NSCL Outreach offers:
Tours for the general public
Summer research programs for middle & high school students
Nuclear science experiments and lessons for teachers to use
For more information online: www.nscl.msu.edu/public/education

## Slide 11: Radioactive, rare isotopes decay
Unstable nuclei are radioactive, meaning they will decay (come apart)…
Gamma ray
…and give off radiation
of some kind!
Alpha particle (He nucleus)
Proton
Neutron
Electron (β- particle)
Isotopes studied at NSCL have short half-lives (< 1 s)

## Slide 12: Radiation Safety
Surveying
Labeling
and Training
NSCL takes radiation safety seriously,
and has met NRC license standards for over 50 years
Fact: NSCL has fewer radioactive sources than a major hospital
Shielding
Notes: In our lab, we use 6-foot-thick concrete to stop radiation from escaping. We’re also very careful to scan for radioactivity and train people how to handle it safely. We checked the tour route to make sure that the radiation levels were safe for you. Radiation is not dangerous when you treat it with respect and know how to manage it. In fact, I walked around the tour route before you got here with a radiation detector to make sure it was safe.

## Slide 13
Radiation source | Dose
Average exposure for general public (natural + medical) | > 300 mRem/yr
Government (NRC) exposure limit for lab visitors | 100 mRem/yr
NSCL/FRIB ALARA goal for visitors | 10 mRem/yr
Your visit today | << 1 mRem
Dental x-ray | 0.5-1 mRem
Smoking a pack of cigarettes | ~2 mRem (800 mRem/yr)
Radiation Exposure and You

## Slide 14: How to make unstable nuclei
NSCL’s Coupled Cyclotron Facility

## Slide 15: Superconductivity
NSCL cyclotrons use electromagnets made from niobium-titanium wires.
At liquid helium temperatures (-269 °C , -450 °F), these wires become superconducting, which means they have zero electrical resistance.
This allows us to make small, powerful electromagnets used to direct and control nuclei!
Superconductors also repel magnetic fields
magnet
superconductor
liquid nitrogen used to cool the superconductor

## Slide 16: The cyclotrons
Year completed: 1982
Diameter: 10 ft Weight: 100 tons
Magnetic field: 3-5 Tesla
Maximum energy it can impart to a proton: 500 MeV
K500
World’s first superconducting cyclotron
K1200
Year completed: 1988
Length of superconducting wire: 38 mi
Time of acceleration: 0.000035 seconds
Distance a nucleus travels while inside: 1.9 miles (700 revolutions)
World’s second-highest-energy superconducting cyclotron

## Slide 17: How a cyclotron works
When stable nuclei from the ion source enter a cyclotron,
a magnetic field bends their path into a circular “orbit” while electric fields speed them up, so they spiral outward
Notes: A cyclotron uses a Magnetic field to steer the nuclei in a circle, and an Electric field to speed it up (that’s why it’s spiraling outward). The K500 speeds nuclei up to 20% of the speed of light and sends them to the K1200, which accelerates them up to HALF the speed of light. How far is that every second?

## Slide 18: Fragmentation
After the target, the beam contains many new isotopes (sometimes <1 desired nucleus/second)
BEAM at < 0.5 c
strikes foil TARGET
exits with FRAGMENTS
The accelerated beam consists of the one stable isotope provided by the ion source
(>1 billion nuclei/second)
or
Very few beam nuclei hit a nucleus in the target and break, becoming a new element/isotope

## Slide 19: Fragment separator
Wedge-shaped dipole magnets act like prisms that separate nuclei
Wide variety of nuclei from collisions with the target enter…
The A1900 filters out all but the one (or more) unstable nucleus for study

## Slide 20: Detectors
“Halo nuclei” and neutron-rich isotopes
MoNA
S800 Spectrograph
Nuclei found in stellar reactions
Nuclear states from particles freed in collisions
HiRA
How do you measure something you can’t see?

## Slide 21: FRIB: Facility for Rare Isotope Beams
MSU has been chosen as the site for FRIB: a $730 million US Department of Energy project to design and establish a world-leading laboratory over the next decade. Civil construction is ongoing, completion by 2022 at the latest.
NSCL today
FRIB design
Notes: 400-yard linear accelerator will replace cyclotrons, producing nuclei with twice the energy and thousands of times more rare isotopes per second
Many additions to the building for personnel, cryogenics, research area, etc.

## Slide 22: FRIB on the MSU campus
Existing NSCL
Target
Highbay
Linac Support Building
SRF Assembly
Ion Sources
SHAW LANE
WILSON ROAD
BOGUE STREET
WHARTON
CENTER


DAIRY STORE
(one
block)
Lobby

## Slide 23: Safety First
DON’T put anything in your mouth (eat, drink, chew gum)
DO obey posted signs
DON’T take photos
DO watch your head and step
DON’T sit or lean on things
DO stay with your guide
DON’T touch equipment
If you lose your tour, dial “0” on a lab phone (“77305” after hours)
DO leave items (especially open food/drink) you don’t want to carry

## Slide 24
sciencefestival.msu.edu
Annually in April
sciencefestival.msu.edu

## Slide 25: National Superconducting Cyclotron Laboratory at MSU
Learn more about our Lab and outreach programs
Get our just-published history Up From Nothing from MSU Press msupress.org or on Amazon
Visit our “Gift Shop” on shop.msu.edu (click on “NSCL/FRIB” under “Specialty Shops”)
Find camps and programs at MSU for
pre-college students: spartanyouth.msu.edu
contact visits@nscl.msu.edu or go to nscl.msu.edu
GIFT SHOP
Get the Android/ iPhone/iPad game Isotopolis for free!
SPARTAN YOUTH PROGRAMS

## Slide 26: FRIB on the MSU campus

## Slide 27: Sources of radiation

## Slide 28: The Control Room
1982
1997
2003

## Slide 29: Behind the scenes at Facility for Rare Isotope Beams
SHAW LANE
BOGUE STREET
More information to be announced at frib.msu.edu
TOURS of the tunnel and experimental areas
Hands-on DEMONSTRATIONS
TALKS by nuclear scientists
FRIB OPEN HOUSE
Saturday, August 18, 11-4pm