## Slide 1: e24joe

## Slide 2: 06/03/2024
New Denisov Paper: https://journals.aps.org/prc/accepted/3e07ePb0E211f9046999039045ee03ba8664a9f1b
212Po alpha decay: https://doi.org/10.1016/j.apradiso.2023.110953
We adjusted the threshold for the south Ge because it was triggering on noise (10 kHz event rate)
We also version controlled the XIA config files so we have a change log of the DDAS parameters
We measured the xyz of the Ge detectors, and took a few calibration runs with 152Eu in different places on the outside of the TPC
We think the ‘mystery blob’ has real events from 212Bi

## Slide 3: 152Eu Ge calibration runs
Once we placed the Ge in the spots they will remain, we took 5 calibration runs:
Run 801: Source on top of TPC, 2.7 cm from MM rim
Run 802: Source on top of TPC, 13 cm from MM rim
Run 803: Source on top of TPC, 40 cm from MM rim
Run 804: Source on side of TPC, across from North
Run 805: Source on side of TPC, across from South

## Slide 4: Germanium Detectors’ XYZ
South:
  31.33 mm from top of TPC to top of Ge
  41.69 mm from MM rim on TPC to edge of Ge
  07.74 mm from front of Ge to side of TPC
North:
  29.88 mm from top of TPC to top of Ge
  113.7 mm from MM rim on TPC to edge of Ge
  04.23 mm from front of Ge to side of TPC

## Slide 5: 228Th Decay Chain

## Slide 6: Gas Test run 0418 (run on 05/24/24, when gas had been flowing all day)

## Slide 7: Gas Test run 0421 (run on 05/29/24 as one of the first runs after not flowing gas for 5 days)

## Slide 8: Run 0003

## Slide 9: Run 0004

## Slide 10: Run 0005

## Slide 11: Run 0006

## Slide 12: Run 0007

## Slide 13: Run 0008

## Slide 14: Run 0010

## Slide 15: Run 0011

## Slide 16: Run 0012

## Slide 17: Run 0013

## Slide 18: Run 0014

## Slide 19: Run 0015

## Slide 20: Run 0016

## Slide 21: Run 0017

## Slide 22: Run 0018 (no 220Rn flow)

## Slide 23: Run 0019 (no 220Rn flow)

## Slide 24: Run 0020 (no 220Rn flow)

## Slide 25: Run 0021 (no 220Rn flow)

## Slide 26: Run 0022 (no 220Rn flow)

## Slide 27: Run 0023 (evacuated upstream)

## Slide 28: Run 0024 (evacuated upstream)
Range limits: 0-80
No range limits

## Slide 29: Run 0025 (evacuated upstream)

## Slide 30: Run 0026 (evacuated upstream)

## Slide 31: Run 0027 (evacuated upstream)
Range limits: 0-80
No range limits

## Slide 32: Run 0028 (Source Still Isolated, flow 24 sccm)
Flow 024 sccm: 0.3779 events/sec

## Slide 33: Run 0029 (Source Still Isolated, flow 175 sccm)
Flow 175 sccm: 0.3314 events/sec

## Slide 34: Run 0030 (Source Still Isolated, flow 521 sccm)
Flow 521 sccm: 0.3187 events/sec

## Slide 35: 228Th Decay Chain

## Slide 36: 2024/06/10

## Slide 37: 241Am and 224Ra Decays
241Am Decays to 237Np, which has a 2.1 million year half-life
241Am has x-rays at 13.9 and 59.54 keV
224Ra has a 241 keV gamma with an intensity of 4% (which we do see in the Ge spectrum)
228Th has gamma 132 keV, 166 keV, 216 keV w/ intensity: 0.127%, 0.101%, and 0.25%

## Slide 38: Evidence of 224Ra? (most likely Lead-212 or Lead-214)

## Slide 39: Look at Mesh and Ge timing spectra (run 0017)

## Slide 40: 2D Hist with Mesh Spectrum and Gamma data (Run 0017)

## Slide 41: Mesh Energy Spectrum and fit (Run 0017) XIA

## Slide 42: Mesh Energy Spectrum and fit (Run 0017) GET

## Slide 43: 2024/06/13 THURSDAY
Sum from -10,000 ns to 15 ns: 197
Sum from 15 ns to 10,000 ns: 222

## Slide 44: Fit Mesh with constrained FWHM

## Slide 45: Increased Flow Rate Tests, source is still bypassed, we are just looking at ‘bg’ (runs 27-30)
Flow 000 sccm: 0.3794 events/sec
Flow 024 sccm: 0.3779 events/sec
Flow 175 sccm: 0.3314 events/sec
Flow 521 sccm: 0.3187 events/sec
Alex and I think that this could be explained by flowing gas in the opposite direction for a while. 228Th decays in that space after the cathode, and when the 220Rn is produced, the higher flow rate carries more of it away
Slightly inconsistent with wall effect changes from runs 16-19 on slides 20-23

## Slide 46: Wall Effect Mystery
When we turn off flow, we see the top line disappear, which suggests to me that these lines are from different decays, not related to location in the chamber where the alpha was created
See runs 16-19 on slides 20-23

## Slide 47: Decay Timestamp plot runs 0018-0030 (fitted with 2 decay curves 10 hours and 3.6 days)
228Th half-life: 1.8 years
224Ra half-life: 3.6 days
220Rn half-life: 55.6 seconds
216Po half-life: 144 ms
212Pb half-life: 10.6 hours
Suggests that we are possibly looking at 228Th

## Slide 48: 2024/06/17 MONDAY
Runs with no Ge data:

## Slide 49: Fit Mesh Spectrum by hand

## Slide 50: Reprocessed Earlier Runs so they are all using the following settings:
Using the config file: ‘p10_2000torr.gui_ini’
RUN 0006 IS GIVING US ERRORS, SEE SLIDE 11 (on fishtank)
Run 7 is able to be reprocessed on fishtank
Run 8

## Slide 51: Some problems processing larger runs
The mac mini has what looks to be 32 GB of ram
Fishtank is a bit more complicated, maybe 12 GB available

## Slide 52: Event estimate
Total events from production runs 1-30: 3.57 million
Conservative estimate would say we have about 1 million alphas from 220Rn, assuming we get ~2.5 alphas per Radon decay

## Slide 53: DNP Abstract
2000 characters long
Use information gathered in my guidance committee meeting as a start

## Slide 54: DNP Meeting Categories:

## Slide 55: Data Estimate

## Slide 56: Looking for 232U in the gamma data

## Slide 57: Python GUI graphical cut

## Slide 58: Testing attpc merger with evt and graw files

## Slide 59: Convection/Diffusion Model for Radon distribution in the TPC active area

## Slide 60: FYI Slides

## Slide 61: CHANGING GAS PRESSURE running ATTPCROOT
For some reason, running the GADGET_II.root macro does not properly replace the two files in the geometry directory required to properly adjust the gas pressure, so I run the following commands to properly adjust the pressure
/mnt/simulations/pxct/joe/gadget/ATTPCROOTv2/macro/Simulation/GADGET$ root -q ../../../geometry/GADGET_II.C; cp GADGET_II.root ../../../geometry/; cp GADGET_II_geomanager.root ../../../geometry/; cd ../../../build/; make; cd ../macro/Simulation/GADGET/; root -q Mg20_test_sim_pag.C; root -q rundigi_sim_Ari.C;

## Slide 62: Evt to root files

## Slide 63: Checking energy resolution at higher pressure with Michael Roosa’s code
Located in /mnt/simulations/proton_detector/michael

## Slide 64: Argonne Cf source
252Cf -> α + 248Cm -> α + 244Pu -> α + 240U -> β + 240Np -> β + 240Pu -> α + 236U -> α + 232Th -> α + 228Ra -> β + 228Ac -> β + 228Th