## Slide 1: e24joe

## Slide 2: 06/03/2024
New Denisov Paper: https://journals.aps.org/prc/accepted/3e07ePb0E211f9046999039045ee03ba8664a9f1b
212Po alpha decay: https://doi.org/10.1016/j.apradiso.2023.110953
216Bi Gammas: https://journals.aps.org/prc/abstract/10.1103/PhysRevC.109.064321
We adjusted the threshold for the south Ge because it was triggering on noise (10 kHz event rate)
We also version controlled the XIA config files so we have a change log of the DDAS parameters
We measured the xyz of the Ge detectors, and took a few calibration runs with 152Eu in different places on the outside of the TPC
We think the ‘mystery blob’ has real events from 212Bi

## Slide 3: 152Eu Ge calibration runs
Once we placed the Ge in the spots they will remain, we took 5 calibration runs:
Run 801: Source on top of TPC, 2.7 cm from MM rim
Run 802: Source on top of TPC, 13 cm from MM rim
Run 803: Source on top of TPC, 40 cm from MM rim
Run 804: Source on side of TPC, across from North
Run 805: Source on side of TPC, across from South

## Slide 4: Germanium Detectors’ XYZ
South:
  31.33 mm from top of TPC to top of Ge
  41.69 mm from MM rim on TPC to edge of Ge
  07.74 mm from front of Ge to side of TPC
North:
  29.88 mm from top of TPC to top of Ge
  113.7 mm from MM rim on TPC to edge of Ge
  04.23 mm from front of Ge to side of TPC

## Slide 5: 228Th Decay Chain

## Slide 6: Gas Test run 0418 (run on 05/24/24, when gas had been flowing all day)

## Slide 7: Gas Test run 0421 (run on 05/29/24 as one of the first runs after not flowing gas for 5 days)

## Slide 8: Run 0003

## Slide 9: Run 0004

## Slide 10: Run 0005

## Slide 11: Run 0006

## Slide 12: Run 0007

## Slide 13: Run 0008

## Slide 14: Run 0010

## Slide 15: Run 0011

## Slide 16: Run 0012

## Slide 17: Run 0013

## Slide 18: Run 0014

## Slide 19: Run 0015

## Slide 20: Run 0016

## Slide 21: Run 0017

## Slide 22: Run 0018 (no 220Rn flow)

## Slide 23: Run 0019 (no 220Rn flow)

## Slide 24: Run 0020 (no 220Rn flow)

## Slide 25: Run 0021 (no 220Rn flow)

## Slide 26: Run 0022 (no 220Rn flow)

## Slide 27: Run 0023 (evacuated upstream)

## Slide 28: Run 0024 (evacuated upstream)
Range limits: 0-80
No range limits

## Slide 29: Run 0025 (evacuated upstream)

## Slide 30: Run 0026 (evacuated upstream)

## Slide 31: Run 0027 (evacuated upstream)
Range limits: 0-80
No range limits

## Slide 32: Run 0028 (Source Still Isolated, flow 24 sccm)
Flow 024 sccm: 0.3779 events/sec

## Slide 33: Run 0029 (Source Still Isolated, flow 175 sccm)
Flow 175 sccm: 0.3314 events/sec

## Slide 34: Run 0030 (Source Still Isolated, flow 521 sccm)
Flow 521 sccm: 0.3187 events/sec

## Slide 35: Run 1

## Slide 36: Run 2

## Slide 37: Run 3

## Slide 38: Run 4

## Slide 39: Run 5

## Slide 40: Run 6

## Slide 41: Run 7

## Slide 42: Run 8

## Slide 43: Run 9

## Slide 44: Run 10

## Slide 45: Run 11

## Slide 46: Run 12

## Slide 47: Run 13

## Slide 48: Run 14

## Slide 49: Run 15

## Slide 50: Run 16

## Slide 51: Run 17

## Slide 52: Run 31

## Slide 53: 228Th Decay Chain

## Slide 54: 2024/06/10

## Slide 55: 241Am and 224Ra Decays
241Am Decays to 237Np, which has a 2.1 million year half-life
241Am has x-rays at 13.9 and 59.54 keV
224Ra has a 241 keV gamma with an intensity of 4% (which we do see in the Ge spectrum)
228Th has gamma 132 keV, 166 keV, 216 keV w/ intensity: 0.127%, 0.101%, and 0.25%

## Slide 56: Evidence of 224Ra? (most likely Lead-212 or Lead-214)

## Slide 57: Look at Mesh and Ge timing spectra (run 0017)

## Slide 58: 2D Hist with Mesh Spectrum and Gamma data (Run 0017)

## Slide 59: Mesh Energy Spectrum and fit (Run 0017) XIA

## Slide 60: Mesh Energy Spectrum and fit (Run 0017) GET

## Slide 61: 2024/06/13 THURSDAY
Sum from -10,000 ns to 15 ns: 197
Sum from 15 ns to 10,000 ns: 222

## Slide 62: Fit Mesh with constrained FWHM

## Slide 63: Increased Flow Rate Tests, source is still bypassed, we are just looking at ‘bg’ (runs 27-30)
Flow 000 sccm: 0.3794 events/sec
Flow 024 sccm: 0.3779 events/sec
Flow 175 sccm: 0.3314 events/sec
Flow 521 sccm: 0.3187 events/sec
Alex and I think that this could be explained by flowing gas in the opposite direction for a while. 228Th decays in that space after the cathode, and when the 220Rn is produced, the higher flow rate carries more of it away
Slightly inconsistent with wall effect changes from runs 16-19 on slides 20-23

## Slide 64: Wall Effect Mystery
When we turn off flow, we see the top line disappear, which suggests to me that these lines are from different decays, not related to location in the chamber where the alpha was created
See runs 16-19 on slides 20-23

## Slide 65: Decay Timestamp plot runs 0018-0030 (fitted with 2 decay curves 10 hours and 3.6 days)
228Th half-life: 1.8 years
224Ra half-life: 3.6 days
220Rn half-life: 55.6 seconds
216Po half-life: 144 ms
212Pb half-life: 10.6 hours
Suggests that we are possibly looking at 228Th

## Slide 66: 2024/06/17 MONDAY
Runs with no Ge data:

## Slide 67: Fit Mesh Spectrum by hand

## Slide 68: Reprocessed Earlier Runs so they are all using the following settings:
Using the config file: ‘p10_2000torr.gui_ini’
RUN 0006 IS GIVING US ERRORS, SEE SLIDE 11 (on fishtank)
Run 7 is able to be reprocessed on fishtank
Run 8

## Slide 69: Some problems processing larger runs
The mac mini has what looks to be 32 GB of ram
Fishtank is a bit more complicated, maybe 12 GB available

## Slide 70: Event estimate
Total events from production runs 1-30: 3.57 million
Conservative estimate would say we have about 1 million alphas from 220Rn, assuming we get ~2.5 alphas per Radon decay

## Slide 71: DNP Abstract
Incorporated Chris’ comments and sent back to him for further revision

## Slide 72: DNP Meeting Categories:

## Slide 73: 2024/06/24 MONDAY
Combined production runs to produce RvE Histogram

## Slide 74: RvE for production runs 1-31 (no veto) early runs with bad gain included
Total number of events: 3,375,536

## Slide 75: RvE for production runs 1-31 (vetoed on >150) early runs with bad gain included
Total number of events: 1,045,905

## Slide 76: RvE with cut on 6 MeV & 150 veto condition
This is 170 hours of data (a little over a week)
We have 737495 events in the 6 MeV blob
Worst case scenario we got 312498 events in that time frame (assuming the Po and Bi alphas have the save efficiency as the Ra alphas)
This means we have a 220Rn decay rate of 1740 per hour, or ~0.48 per second (as a lower bound)
Does this mean we can increase the flow rate? We based our current flow rate on the fact that our GET DAQ is collecting 5 events per second, which of course has no veto condition

## Slide 77: RvE with cut on 8 MeV & 150 veto condition
Total non-vetoed events in the 8 MeV blob: 75233

## Slide 78: Run 31 was the first run we introduced the source after a week of isolation
Events in the 8 MeV: 5804
Events in the 6 MeV: 102833
6-8 Ratio in run 31: 17.718
6-8 Ratio in production runs 1-31: 9.8028

## Slide 79: Run 1 Event 155318 (crosstalk between vetos and adjacent pads)

## Slide 80: Run 3 Event 1093

## Slide 81: Run 3 Event 1614

## Slide 82: Run 5 Event 50650

## Slide 83: Run 5 Event 85566

## Slide 84: Run 5 Event 103991

## Slide 85: Run 5 Event 110804

## Slide 86: Run 5 Event 113758

## Slide 87: Run 5 Event 162886

## Slide 88: Run 5 Event 245601

## Slide 89: Run 5 Event 295365

## Slide 90: Run 5 Event 324309

## Slide 91: Run 5 Event 326950

## Slide 92: Run 7 Event 65771

## Slide 93: Run 7 Event 90308

## Slide 94: Run 8 Event 165420

## Slide 95: Run 8 Event 261100

## Slide 96: Run 10 Event 160001 (Double Alpha?)

## Slide 97: Run 10 Event 258053

## Slide 98: Run 12 Event 176748

## Slide 99: Run 14 Event 23030

## Slide 100: Run 14 Event 53275

## Slide 101: Run 14 Event 71891 (?)

## Slide 102: Run 14 Event 247782 (accidental coin?)

## Slide 103: Run 15 Event 137612 (scatter?)

## Slide 104: Run 16 Event 110785

## Slide 105: Run 16 Event 152872

## Slide 106: Run 31 Event 63736

## Slide 107: Run 31 Event 193219

## Slide 108: Run 31 Event 213088

## Slide 109: I want to confirm the back half of the decay chain is mainly decaying on the cathode

## Slide 110: Same plot as previous slide with veto condition enabled

## Slide 111: Plotted Angular distribution weighted by 1/sin(theta)

## Slide 112: 2024/06/27 THURSDAY
Gated Range spectrum on 6 MeV blob
Efficiency Sims for 220Rn uniform dist, 216Po & 212Po on cathode, and double alpha

## Slide 113: Cut on 6 MeV blob and looked at range projection to see if we can distinguish peaks

## Slide 114: ATTPCROOT Efficiency Sim to determine ratio of detected events
When I set the decays to occur only on the cathode, I get an efficiency of 37% (this is for uniform dist., beam dist. gives an efficiency of 98%)
This means that we probably are not simulating alphas that run into the border
In the calculate efficiency script, I add the number of vetoed events and the number of events with 0 hits on the pads to get total ‘missed events’. For 1,000 simulated 212Po events, we get:
  542 0 hits (likely decayed into the cathode)
  340 vetoed events
  8.784 MeV 212Po alpha efficiency on the cathode of: 11.8%
For 6.7783 MeV 216Po on the cathode:
  541 0 hits
  300 vetoed events
  6.7783 MeV 216Po alpha efficiency on the cathode of: 15.9%
For 6.288 MeV 220Rn uniformly distributed:
  87 0 hits
  636 vetoed events
  6.288 MeV 220Rn alpha efficiency on the cathode of: 27.7%
For double alpha uniform dist. (upper limit because we are including partial cathode events hits > 0):
  22 0 hits
  866 vetoed events
  6.288 MeV 220Rn alpha efficiency on the cathode of: 11.2%

## Slide 115: Using PCA to extract ranges (run_0017)

## Slide 116: Data Estimate (up to run 46)
Total non-vetoed events: 2,995,764
Events in 8 MeV peak: 227,845
Events in 6 MeV peak: 2,235,169
Estimated 220Rn decays detected (using 6 MeV peak and assuming everything but 220Rn decay on the cathode in a uniform dist.): 1,255,960
Zhao predicts a BR of 10-6.4, so to get 1 double alpha events, we need to decay 2.51 million 220Rn.
To get 10 non-vetoed double alpha decays to occur (taking into account their efficiency compared to a single alpha 220Rn decay) we need 60 million 220Rn alpha decays. At our current rate, that would require to run for 66 weeks
We probably want a higher event rate to complete this experiment
We do not want to go above 30 non-vetoed events per second, as that is when our rate limiting bg is on the same order of magnitude as the BR predicted by Zhao
Flow rate -> Event rate
174 sccm gives 5 events/sec (vetoed + nonvetoed)
244 sccm gives 14 events/sec (vetoed + nonvetoed)
324 sccm gives 25 events/sec (vetoed + nonvetoed)
All events (no veto condition)
Non-vetoed events (veto<150)

## Slide 117: Processing Run 49 gave this message, but seemed to complete the processing

## Slide 122: Gain matching GET energy spectra on a sub run basis

## Slide 123: Tchain gamma data together to look for alpha-gamma events

## Slide 124: Looking for 232U in the gamma data

## Slide 125: Python GUI graphical cut

## Slide 126: Testing attpc merger with evt and graw files

## Slide 127: Convection/Diffusion Model for Radon distribution in the TPC active area

## Slide 128: FYI Slides

## Slide 129: CHANGING GAS PRESSURE running ATTPCROOT
For some reason, running the GADGET_II.root macro does not properly replace the two files in the geometry directory required to properly adjust the gas pressure, so I run the following commands to properly adjust the pressure
/mnt/simulations/pxct/joe/gadget/ATTPCROOTv2/macro/Simulation/GADGET$ root -q ../../../geometry/GADGET_II.C; cp GADGET_II.root ../../../geometry/; cp GADGET_II_geomanager.root ../../../geometry/; cd ../../../build/; make; cd ../macro/Simulation/GADGET/; root -q Mg20_test_sim_pag.C; root -q rundigi_sim_Ari.C;

## Slide 130: Evt to root files

## Slide 131: Chain loading root files
In /mnt/analysis/e21010/sun
analysis_chain_sorted_e21010.C
analysis_chain_unpacked_e21010.C
These two look very similar to me. One is for their raw root; one is for their calibrated root, I think.
I looked at the cal.root file size; simply hadd all runs should be fine.

## Slide 132: Checking energy resolution at higher pressure with Michael Roosa’s code
Located in /mnt/simulations/proton_detector/michael

## Slide 133: Argonne Cf source
252Cf -> α + 248Cm -> α + 244Pu -> α + 240U -> β + 240Np -> β + 240Pu -> α + 236U -> α + 232Th -> α + 228Ra -> β + 228Ac -> β + 228Th