## Slide 1: Design and Simulation of a Proton Detector for studying low-energy resonances relevant in thermonuclear reactions
David Perez-Loureiro
NSCL, Michigan State University
Collaborators: C. Wrede, E. Pollacco and the AstroBox collaboration

## Slide 2: Outline
Motivation
Conceptual Design
MicroMEGAS Detectors
Detector Simulations
Physics Case: 31Cl(bp)30P
Summary and Outlook

## Slide 3: Motivation
White dwarf (Novae) or neutron star (type I X-ray burster) accreting H from binary companion
Temperature increases without expansion
Compression ignites thermonuclear runaway at surface and nucleosynthesis
Temperatures up to 0.4 GK (Novae) and 2 GK (type I X-ray burst)
Uncertainties in the reaction rates need to be constrained for modelling
Nova Cygni 1992 (in 1994) NASA, ESA, HST
Credit: David A. Hardy/http://www.astroart.org & PPARC
Notes: X-ray bursters are explosions on the surface of neutron stars which accrete material from a companion star in a stellar binary system. They are characterised by intense short-lived bursts of X-rays. A key question about such explosions is the trigger for the break-out from the hot-CNO cycle into the rp-process.
There are a number of reactions of interest in terms of the break-out from the hot-CNO cycle. These include 15O(α,γ), 14O(α,p) and 18Ne(α,p). Ideally, we would study these reactions directly and obtain astrophysical reaction rates for them for the complete temperature regime of interest. In practice, this is extremely challenging as each of the nuclei are short-lived radioactive species. Such nuclei can be produced as accelerated radioactive beams at facilities such as Oak Ridge National Laboratory in the US, REX-ISOLDE in CERN, ISAC in Vancouver and CRIB in Japan. It has not been possible, however, to obtain these beams with sufficient intensity to make direct measurements with a useful precision, or at energies corresponding to sufficiently low temperatures.

## Slide 4: Nucleosynthesis in novae
Proton captures and b-decays
rp process in ONe novae up to A=40
30P(p,g)31S reaction is a potential bottleneck for nucleosynthesis (t1/2=2.5 min)
Reaction rate needs to be constrained experimentally
Dominated by resonant capture
Can’t be measured directly because of low intensities available of 30P beams
Indirect methods
J. Jose et al., ApJ 494,680,(1998)
30P(p,g)31S

## Slide 5: Nucleosynthesis in novae
Novae as possible origin of pre-solar grains 30Si/28Si
Novae “thermometers”
4 mm presolar SiC crystal from the Murchison meteorite.
Credit: S. Amari
L. N. Downen et al. ApJ 762 105 (2013)

## Slide 6: Nucleosynthesis in type I x-ray bursts
H/He Burning via standard and “Hot” CNO cycles
15O(a,g)19Ne is one of the two routes to break out CNO cycles and trigger rp-process in type I x-ray bursts for nucleosynthesis of A>20 nuclides
Can’t be measured directly either because of low intensities available of ISOL 15O beams
Energies of future reaccelerated fragmented beams much higher than the energies required (~150 keV)
3
4
5
6
7
8
9
10
11
12
13
14
C (6)
N (7)
O (8)
F (9)
Ne (10)
Na (11)
Mg (12)
3a process
15O(a,g)19Ne
Neutron Number
Proton Number
HOT CNO cycle

## Slide 7: Indirect measurements
b-delayed particle and g emission
Excited stated of the nucleus of interest populated in beta-decay of precursor over the particle emission threshold
Need to measure Er,Gg,Gp and Jr
AY
AX
A-1Z+p
E
b2
b1
g1
g2
g3
g4
p1
p2
p3
Sp

## Slide 8: Detector requirements
Ability to detect b-delayed ps and as as low in energy as possible with high efficiencies because Gparticle << Gg at low energies due to Coulomb and centrifugal barriers
Beta energy deposition: can cause background and summing (Silicon detectors)
Need to distinguish b-p from b-p-g
Multi-charged-particle emission
Want detector chamber to fit inside cylindrically-symmetric SeGA array, which has an inner diameter of 18cm
Want sensitivity to protons and alphas below 200 keV (ideally beta background stops at 150 keV)
SeGA

## Slide 9: MicroMEGAS Detectors
Drift Region
  Particles ionize the gas along their trajectories
  Electrons drift to anode pads under an applied field (~100 V/cm)
Amplification Region
  Avalanche multiplication
  Signal induced in readout pads
  Fast timing, robust, cost effective, good energy resolution
HV1
HV2
E1
100 V/cm
E2
50 kV/cm
10 cm
100 mm
Cathode
MicroMesh
Drift Region
Amplification Region
Readout Pad
b
ne
p
e-
e-
e-
e-
Y. Giomataris et al. Nucl. Instr. and Meth. A, 376 (1996), p. 29
e-

## Slide 10: AstroBox detector
E. Pollacco et al. Nucl. Instr. and Meth. A, 723 (2013), p. 102
Similar detector already used at Texas A&M University Cyclotron
Successful operation with 23Al beam
Same technology based on MGPDs

## Slide 11: NSCL ProtonDetector Simulation
Based on Geant 4.9.6 and ROOT 5.34
Realistic input distributions based on LISE++ calculations
Different geometries available
Information of the track of all particles inside the gas stored in a ROOT file
http://geant4.web.cern.ch/geant4/
http://root.cern.ch
http://lise.nscl.msu.edu/lise.html

## Slide 12: Event generation
Two step simulations: Implantation+Decay
Initial beam properties calculated with LISE++ and inserted in GEANT
Decay: Initial position distribution from Implantation stage
X Position [mm]
Z Position [mm]

## Slide 13: Simulation of drift, amplification and digitization of MPGDs
  Calculation of primary electrons from energy deposited at each interaction step with Poisson fluctuation.
  Randomization of the final position at the anode according to transversal diffusion coefficients for each of the electrons produced (Charge spread)
  Gain fluctuations calculated for each electron using the Polya distribution.
  Charge collected on pads is the sum of all the ionization electrons produced + noise.
  Charge threshold applied.
(xi,yi,zi,ti,DEi)

## Slide 14: Proposed Geometry
Cylindrical detector
 180 mm x 200 mm length
Keeps the symmetry of SeGA array rings
Central pad ( 60 mm) + 4 sectors (120 mm), perpendicular to the beam axis

## Slide 15: Performance
b
p
Beta contribution lower than 150 keV
Resolution 6.5% FWHM at 200 keV
Protons+Betas
Protons
Betas
23Al b-delayed proton emission
95%Ar 5% CH4 @ 800 torr

## Slide 16: Detection efficiency for protons
Total efficiency ~100% up to 1 MeV
Central pad efficiency >65% at energies <800 keV
95%Ar 5% CH4 @ 800 torr

## Slide 17: Physics Case: 31Cl(bp)30P
31Cl b-delayed gamma emission measured at NSCL e12028 (analysis ongoing)
6.39 MeV state in 31S populated via b-decay (~1%)
31S
31Cl
30P+p
E (keV)
Sp=6131
6391
6937
7037
7157

## Slide 18: Physics Case: 31Cl(bp)30P
31S
31Cl
30P+p
E (keV)
Sp=6131
6.39 MeV state in 31S populated via b-decay (~1%)
Gp/Gg~3.2x10-6
6391
Protons+Betas
Betas
780 keV
870 keV
993 keV
1520 keV
260 keV
6937
7037
7157

## Slide 19: Physics Case: 31Cl(bp)30P
Background disappears in the region of interest with anticoincidence condition
Efficiency drops at E>1MeV
Protons+Betas
Betas
780 keV
870 keV
993 keV
1520 keV
260 keV
31S
31Cl
30P+p
E (keV)
Sp=6131
6391
6937
7037
7157

## Slide 20: Summary and Outlook
Simulation developed is operative and running
Beta background as low as 150 keV
Energy resolution below 7% FWHM at 200 keV
Highly suppressed background for higher energies by anticoincidence
Next Steps:
  Define final geometry.
  Electrostatic calculations for the field cage (GARFIELD)
  Investigate position sensitive pad planes for multi particle emission to study 15O(a,g)19Ne via 20Mg(bpa)15O (TPC)
  Add gamma detectors to simulation
  Test with MicroMEGAS prototypes
  Commissioning experiment with 23Al (sensitivity) and 32Ar beams (efficiency)

## Slide 21: Backup Slides

## Slide 22: 20Mg(bpa)15O
More Segmented pad plane (Position sensitive)
Particle ID based on diferent ranges on gas
e.g. P10 1 atm
Protons 2.7 cm
Alphas 0.32 cm

## Slide 23: 23Al(bp)
197 keV
554 keV
828 keV
Protons+Betas
Betas
Background disappears applying Anti-Coinc for E>150 keV

## Slide 24
30Si
28Si
30P(p,g)31S